## Slide 1: WEB PAGE SMART ROBOT (Robot controlled by web page using ESP32)
Presented by:
T .Madhuri
B .Rajitha
V .Prameela
S .Aishwarya

## Slide 2: List of contents
Introduction
Components
Block diagram
Working principle
Applications
Advantages
Conclusion

## Slide 3: Introduction
This project showing how to control the Robot by using an ESP32 development board with Arduino IDE. Here using a motor driver L293D. This module allows us to control the speed and direction of the motors.
And also to know about the temperature in our surroundings using DHT11.
By using IR sensor we will find which type of gas is present in the atmosphere.

## Slide 4
Components Required
ESP32 Development board
DC motor
L293D motor driver
IR sensor
Gas sensor
Buzzer
Connecting wires
Jumper wires(as required)

## Slide 5
Block Diagram
ESP32
Gas sensor
DHT11
Power supply
IR sensor
Buzzer
Web page
Robot
Thing
speak

## Slide 6: Working Operation
We’ve shown you how to control the direction and speed of a DC motor using an ESP32 and the L293D motor driver.
Write the code for developing the web page.
After developing the clients web page then connect the USB cable to the ESP32 board and DC motor.
The motor we’ll control is connected to the motor A output pins, so we need to wire the INPUT1 and INPUT2 pins of the motor driver to the ESP32.
Follow the wire the DC motor and the L293D motor driver to the ESP32.

## Slide 7
To control the direction the DC motor is spinning you use the input 1 and input 2 pins.
Apply LOW to input 1 and HIGH to input 2 to spin the motor forward. Apply power the other way around to make it spin backwards.
Also connect the gas sensor IR sensor and LM35 to know about temperature and any poisonous gases in the surroundings . Also connect the buzzer.
After that the sensor will be sense the temperature and poisonous gases .The temperature will be shown in the web page and graph will be shown in thing speak . If any poisonous gas is detected by gas sensor then the buzzer will make some noise.

## Slide 8
Applications
It is used in coal mines.
It is used in industrial purpose.

## Slide 9: Advantages
It can be used wherever people cannot go or where things doing too dangerous for humans to do safely.
The presence of bio hazardous gases were detected through Gas Sensor which is placed at the robot.
This system can be used where ever the safety and security are the major threat.

## Slide 10: Conclusion
One of the main things we found was that anything the robot can do.
This is very cheap and efficient project .